## Slide 1: Addresses
The Findability factor in OpenStreetmap
This document licensed in entirety by Creative Commons CC-by-SA. For specific terms of license, see: http://creativecommons.org/licenses/by-sa/3.0/

## Slide 2: Overview
What is an Address and Why Do We Care?
Characteristics of US Addresses
Why We Need to Expand Our Tagging
How to Improve Our Address Tagging Practice
Benefits to the OSM Community

## Slide 3: Addresses vs. Address Ranges
Addresses are point features
  Uniquely apply to one place (mostly)
  1:1 match description to coordinates
  May reference a street (or linear feature)
Address ranges are linear features
  Describe a sequence of addresses
  Associated with a street (or linear feature)
Our concern here is with address points

## Slide 4: Why care about addresses?
Addresses are the most granular geographic features
Support routing – E911 & Emergency Services
Support supply chain management – Delivery
Support work order management - Logistics
Support statistics and surveys – Census, Polling
Numerous navigation, wayfinding, and mental maps

## Slide 5: Characteristics of US Addressing Practice
US has several street naming schemas:
  Quadrant system – base lines dividing city into sections
  Coordinate, or Lyman system – Addresses reference numbered streets to provide relative coordinates
  Theme/alphabetical – Presidents, natural features, place names, etc. Alphabetical sequencing
  Neighborhood Unit – Self-contained neighborhoods with thematic street names (local landmarks, historical events, etc.)
US has numerous property numbering schemas
  Frontage intervals
  Block intervals
  Decimal

## Slide 6: US Street Naming schemas
Quadrant System
  Divides city into four quadrants on baseline streets
  Streets numbered/ named off of baseline
Image source: Alachua County, FL

## Slide 7: US Street Naming schemas
Lyman, or Coordinate System
  Baseline streets on grid
  Numbered streets in 100’s
  Complicated, but useful without a map

## Slide 8: US Street Naming schemas
Neighborhood Unit
  Subdivisions, or areas where topography does not lend itself to grid
  Local landmarks, historical events, thematic

## Slide 9: US Street Naming schemas
Alphabetical Sequencing
  Alphabetical order
  Multiple syllables used to overcome limits of 26 character alphabet
Image source: Matt Johnson @tracktwentynine

## Slide 10: Property Numbering: Frontage Intervals
Source: City of Muncie, IN Uniform Numbering Code
  SECTION 156.05: AXIS AND PROGRESSION
The first numbers on Walnut Street at Main Street shall be in the 100 series and shall increase to the north and south therefrom but shall not exceed 100 numbers to each block; 16 blocks to the mile, or approximately 330 feet per block. The first numbers on Main Street at Walnut Street shall be in the 100 series and shall increase to the east and west therefrom but shall not exceed 100 numbers to each block; 16 blocks to the mile, or approximately 330 feet per block. Whenever a block is not 330 feet the block series for this segment shall be established at local intervals as the case may require.

## Slide 11: Property Numbering schemas
Century, or Equal Interval System
Image source: Osoyoos Ordinance

## Slide 12: Property Numbering: Philadelphia Blocks
Image source: Reuben S. Rose-Redwood
Philadelphia blocks, or decimal system
  Metric blocks

## Slide 13: What to Conclude?
In the US, there is a high degree of local variation
  …in street naming schemas
  …in property numbering schemas
There is unlikely to be any US national street naming/property numbering schema
  Local control is well-established
  US National Grid is too cumbersome for most people
Need the ability to accurately describe any system of addresses

## Slide 14: Limitations of Current Practice
Addresses in the US do not increment uniformly by 2
  Implications for interpolation
Tag addr:street is overloaded with:
  Street Name
  Street Type
  Directional prefix
  Directional suffix

## Slide 15: Limitations of Current Schema
Tagging in current (& widespread) usage is unsuitable for variety of address schemas
  Not descriptive of local conditions
    Cities with Lyman systems (e.g. Salt Lake City), hard to parse street names
    Street name and street type combined in one tag
  Expand? Or, not expand?
    “Saint” vs. “St.” vs. “Street”
    “Northwest” vs. “NW”
  Ambiguous Street Names
    “The Plaza” – Charlotte, NC
    “Boulevard” – Richmond, VA

## Slide 16: What do we need from an Address Schema?
The premise of a good address schema should be:
  Flexible
  Descriptive
  Understandable
  Granular
  Reflect local practice

## Slide 17: Proposed Tags for Addresses
The addition of three tags
  addr:street_type – e.g. ‘Avenue’, ‘Street’, ‘Lane’, ‘Drive’, ‘Road’, etc.
  addr:dir_pre – Directional prefix, e.g. ‘N, ‘North’, ‘NW’, ‘Northwest’, etc.
  addr:dir_suf – Directional suffix, e.g. ‘S’, ‘South’, ‘SE’, ‘Southeast’, etc.
Limit the use of addr:street
  Name of street ONLY

## Slide 18: Examples
Sample Address: “6345 W. Euclid AV”
  addr:housenumber = “6345”
  addr:dir_pre = “W”
  addr:streetname = “Euclid”
  addr:street_type = “Avenue”
Sample Address: “468 13th St NE”
  addr:housenumber = ‘468’
  addr:streetname = ‘13th’
  addr:street_type = ‘Street’
  addr:dir_suf = ‘NE’

## Slide 19: What are the Benefits?
Expands the descriptive power of addresses…
  More granularity
  Less overloading of tagging schema (e.g. addr:street
  Minimal increase in effort
Better reflect the way US addresses are assigned
  Consistent with local government practice
  Facilitate local government as address data source
More accurate description of local conditions
  Greater flexibility accommodates variations in local practice

## Slide 20: Summary
Street naming and address assignment vary widely across the US
  Local variation in schemas
  Local authority for addressing
Current practice is inadequate
  Omits valuable data
  Inflexible for local conditions
Adding just three tags yields great improvements
  Greater descriptive power
  Flexibility for local mappers

## Slide 21: Addressing References/Resources
Address Improvement Wiki Page

## Slide 22: Addressing References/Resources
Street-Naming and Property Numbering Systems. Margaret A. Corwin. Planning Advisory Service, Report No. 332.
US Thoroughfare, Landmark, & Postal Address Data Standard
  http://www.fgdc.gov/standards/projects/FGDC-standards-projects/street-address/FGDC_endorsedAddressStandard.zip
Governmentality, the Grid, and the Beginnings of a Critical Spatial History of the Geo-coded World. PhD dissertation, Reuben S. Rose-Redwood
  https://etda.libraries.psu.edu/paper/6981/2245

## Slide 23: Thank You
Questions?
Steven Johnson
  (e) sejohnson8@gmail.com
  (t) @geomantic
This document licensed in entirety by Creative Commons CC-by-SA. For specific terms of license, see: http://creativecommons.org/licenses/by-sa/3.0/